## Slide 1: Linear Measurement

## Slide 2: Linear Measurement
Measurement of perpendicular distance Between two points or surfaces. Designed either for line measurements or end measurements
Applies to measurement of length, heights, diameters, thicknesses, radius etc.
Line measuring instruments consists of series of accurately, spaced painted or marked lines on them

## Slide 3: Linear Measuring instruments
(A)Classification based on methods of measurement
l. Direct measuring instruments.
2. Indirect measuring instruments.
Measuring instruments can be further classified as :
  Graduated instruments. It includes rules, vemier callipers, vernier height gauges, vernier depth gauges, micromètres, dial indicators etc.
  Non-graduated instruments : It includes callipers,, wire gauges, screw pitch gauges, radius gauges, thickness gauges, slip gauges etc.

## Slide 4: Graduated instruments

## Slide 5: Non-graduated instruments
Callipers
Wire gauges
Screw pitch gauges
Notes: Presenter
2016-02-12 14:19:36
--------------------------------------------
mp1

## Slide 6: Linear Measuring instruments
(B) Classification based on the accuracy that can be obtained
l. Non-precision type instruments : It includes steel rule, caliper, divider; depth gauge, telescopic gauge etc.
2. Precision type instruments :It includes vernier calliper, vernier height gauge, vernier depth gauge, micrometer, slip gauges, etc.

## Slide 7: Steel Rule

## Slide 8: Least Count
Capability of an instrument to measure minimum distance accurately.
It represent the accuracy of measurement
Difference between the value of main scale division and auxiliary scale division.
Least count of vernier instruments
 L.C. of vernier instruments also can be calculated as

## Slide 12: Working
Vernier calliper

## Slide 16
Vernier principle : When two scales (main and auxiliary scales) or division slightly different in size are used, the difference between them can be utilized to enhance the accuracy of measurement.
Construction :

## Slide 18: Errors in vernier calliper :
Errors due to play between the sliding jaw and fixed scale bar.
Error due to wear and wrapping of jaws.
Errors due to incorrect observation of scale readings
Errors due to excessive force on moving jaw.
Error is also introduced if the line of measurement does not coincide with the line of the scale

## Slide 19
Precautions to be taken in use of vernier calliper :
No play should be there between sliding and fixed jaws. If play exists then the accuracy of the vernier calliper will be lost.
The tips of measuring jaws should not be worn . (3)Use the stationary jaw on reference point and obtain
measured point by sliding the movable jaws.
The vernier calliper must always be properly balanced in hand and held lightly the sliding jaw through adjusting screw. Do not push the moving jaw, under pressure, use adjusting screw for fine adjustment.
In case of measuring an outside diameter, be sure that calliper bar and the plane of Calliper jaws are truly perpendicular to the work piece's longitudinal centre line.

## Slide 20: Vernier height guage
Similar to a vernier calliper except that the fixed jaw in this case is replaced by a fixed base which rests on a surface plate or table when taking measurements.
Precautions to be taken in use of vernier height gauge
It should be tested for straightness, squareness, and parallelism of working beam, measuring jaw and scriber.
base is clean and free from burrs.

## Slide 21: Vernier depth gauge