## Slide 1
An overview of
LINE BALANCING

## Slide 2: A SIMPLE LINE FOR PRODUCTION OR ASSEMBLY
Workstation 1
Workstation 2
Workstation 3
Workstation 4
Input
Output

## Slide 3: ACTIVITY CLASSIFICATION
Value Adding:
Any process that changes the nature, shape or characteristics of the product, in line with customer requirements e.g. machining, assembly
Non-Value Adding, but unavoidable with current technology or methods:
Any work carried out that does not increase product value e.g. inspection, part movement, tool changing, maintenance
Waste:
All other meaningless, non-essential activities that do not add value to the product you can eliminate immediately
e.g. looking for tools, waiting time

## Slide 4: WASTES
Wastes are caused from:
Transportation
Inventory
Motion
Waiting
Overproduction
Over-processing
Defects
(The 7 Wastes: T.I.M.W.O.O.D)

## Slide 5: UNBALANCED LINE : SIMPLE EXAMPLE
1
2
3
4
15 mins
10 mins
Constraint Overburden
This operator must WAIT for operator 2
Overproduction which causes the other 6 wastes
5 mins 25 mins
Over-processing
Inventory Waiting
defects
Transportation
Motion
This operator must WAIT for operator 3
1
2
3
4
25
20
mins 15
10
5

## Slide 6
LINE BALANCING: DEFINITION
Line Balancing is the process of assigning tasks to workstations in such a way that the workstations have approximately equal time requirements.

## Slide 7: LINE BALANCING: OBJECTIVES
Main Objectives:
to equalize the work load among the operators
to identify the bottleneck operation
to establish the speed of the production line
to determine the number of workstations
to determine the labor cost of production and pack out
to establish the percentage workload of each operator
to assist in plant layout
to reduce production cost

## Slide 8: LINE BALANCING: METHODS
There are many ways or methods for balancing the lines.
The common thing for all this methods is:
using both the operator and the machine in the most efficient way, at the same time providing flexibility in production.

## Slide 9: BALANCED LINE: SIMPLE EXAMPLE
25
20
15
10
5
Redistribute the work
1
2
3
4
15 mins
15 mins
15 mins
10 mins
Promotes one- piece FLOW
Avoids overburden
Minimises the 7
wastes
Reduces Variation

## Slide 10
Cycle time : The maximum time allowed at each workstation to complete its set of tasks on a unit.
The number of workstations

## Slide 11: CONCEPTS
Bottleneck: The work station taking the longest time. In production and project management, a bottleneck is one process in a chain of processes, such that its limited capacity reduces the capacity of the whole chain.
Required Cycle Time:
Current Cycle Time: The same as Bottleneck Time.
Flow Time (Total Work Content): Time to complete all stations.
1 2 3
2min 5min 3min
Flow time= 2+5+3=10min Current cycle time = 5min
Bottleneck

## Slide 12: CONCEPTS
A
H
D
E
Precedence diagram: Network showing order of tasks and restrictions on their performance.
B
F
G
Total work content: Sum of the task times for all the production tasks for the product.
Minimum number of work stations=
The quotient should be rounded to the next highest integer.

## Slide 13: LINE BALANCING: PREREQUISITES
9-12
 Determine minimum rational work elements.
(Smallest feasible division of work)
 Determine cycle time.
 Calculate the theoretical minimum number of
work stations.
 Draw Precedence Diagram

## Slide 14: LINE BALANCING: A SIMPLE ALGORITHM
Identify tasks whose predecessors have been assigned to a
workstation (available tasks).
Determine from available tasks, those that fit, i.e., those whose tasks times time remaining to be filled at this work station.
Choose a task that fits by some decision rule
  task with largest time
  task with most successors
  task with greatest sum of task times of its predecessors.
Continue steps 1 to 3 until no task fits, then go on to next workstation.
Continue steps 1 to 4 until all tasks are assigned

## Slide 15: LINE BALANCING: EXAMPLE
Task | Task Time (sec) | predecessors
A | 70 | -
B | 80 | A
C | 40 | A
D | 20 | A
E | 40 | A
F | 30 | B,C
G | 50 | C
H | 50 | D,E,F,G
Total: | 380 | 

## Slide 16: LINE BALANCING: EXAMPLE
Current Conditions:
Current Cycle Time= Bottleneck Time = 80 sec
Current No. of Workstations : 6
Total Product Per Day =
(total time available per day)/(cycle time)
= (8×3600)/(80) = 360 units
A
B
C,D
E,F
G
H
70 sec
80 sec
70 sec
50 sec
60 sec
50 sec
Wanted Total Product is 320 Units Per Day (Consider 8 hrs shift)

## Slide 17: LINE BALANCING: EXAMPLE
According To The Problem:
Cycle Time = (8×3600)/320 = 90 sec
Total Work Content = 380 sec
No. of Workstations = 380/90 = 4.22
5

## Slide 18: LINE BALANCING: EXAMPLE
Precedence Diagram:
A
F
70 sec
H
50 sec
G
50 sec
30 sec
E
40 sec
D
20 sec
C
40 sec
B
80 sec

## Slide 19: LINE BALANCING: EXAMPLE
Task | Task Time | Task time + follower task times
A | 70 | 380
B | 80 | 160
C | 40 | 170
D | 20 | 70
E | 40 | 90
F | 30 | 80
G | 50 | 100
H | 50 | 50
B
A
70 sec
H
50 sec
G
50 sec
F
30 sec
E
40 sec
D
20 sec
C
40 sec
80 sec
Workstation
2
Workstation
3
Workstation
5
Workstation
4
B
H
80 sec
70 sec
50 sec
Workstation
1
A C
D G
90 sec 90 sec
E
F

## Slide 20: LINE BALANCING: EXAMPLE
Comparing Line Efficiency:
Line Efficiency =(Total Work Content)/(No. of Workstations ×Cycle Time)
Case 1: Line Efficiency = (380)/(6×80) = 79%
Case 2: Line Efficiency = (380)/(5×90) = 84%

## Slide 21: PARALLEL WORKSTATIONS
1 min.
2 min.
1 min.
1 min.
30/hr.
30/hr.
30/hr.
30/hr.
1 min.
1 min.
1 min. 1 min.
60/hr.
30/hr.
30/hr.
60/hr.
1 min.
30/hr.
30/hr.
Bottleneck
Parallel Workstations

## Slide 22
Value
Added
Waste
Traditional Focus
Work Longer-Harder-Faster
Add People or Equipment
Lean Manufacturing
Improve the Value Stream to Eliminate Waste
LEAD TIME